## Slide 1
FlowQoS: Not Every Flow is Born the Same
Group 20: Dhruv Sharma, Robert Jenkins, Frederik Nygaard, Feichao Qian
Efficient Bandwidth Utilization
Motivation
Solution
Traffic from one application might not share the same characteristics as the traffic from another.
Network devices have DSCP-based QoS requiring applications to set the corresponding fields in IP header.
Isolate different traffic using OpenFlow in separate queues each rate limited using OVS ingress policing to it’s user-specified bandwidth share.
Use Linux's advanced routing and traffic control to prevent under-utilization of available bandwidth.
Improvements to Application Performance using OVS-Openflow Classification
Additional Gains from using Hierarchical Token Bucket (HTB) in Linux Traffic Control
Reduced Skype Call Jitter
Improved VLC Real-time Streaming Bitrate
Reduced Frame Drops and Segment Latency in DASH (HTTP) Video Streaming
Improved Worst-Case VLC Streaming Bitrate
Reduced Latencies in DASH Video Streaming
OVS-OpenFlow Policing Bandwidth Utilization
HTB Traffic Shaping Bandwidth Utilization
FlowQoS Classification & Rate Control
Linux Traffic Control
Users configure priorities for specific high-level applications.
The output from the portal is a configuration file that the rate shaper uses for shaping traffic.
Enables per-class QoS by creating a two-switch virtual topology.
Each link corresponds to a different traffic class and is rate-limited to the user‐specified rate.
Classification uses DNS records for HTTP traffic and first 4 bytes of the flow in either direction.
Provides a handle tc for Linux kernel’s network scheduler for low-level manipulation of network traffic flowing through it.
Implements multiple queuing disciplines, traffic policers and shapers to provide QoS to matching traffic.
HTB is classful queueing discipline that supports multi-level traffic classification and shaping on egress traffic at an interface.
FlowQoS Architecture
Heirarchical Token Bucket (HTB) Traffic Flow
Results
Conclusion & Future Work
FlowQoS improves performance and user experience for time-sensitive applications.
HTB-based solution smoothens traffic and improves bandwidth usage but might increases latencies.
Use OVS’s NetFlow support for metering and analytics.
Use SFQ discipline for equal share within each queue.